## Slide 1: Open Shortest Path First (OSPF): Introduction

## Slide 2: Introduction to OSPF
» Open standard
» SPF (shortest path first) algorithm
» Hello used for neighbor relationship
» Most packets sent to multicast address of 224.0.0.5 or 224.0.0.6
» Works based on area hierarchy, minimizes LSA flooding
» Supports clear-text and MD5 authentication

## Slide 3
OSPF LSAs
» LSA = Link State Advertisement
» Carried within an OSPF Link State Update Packet
» Different types carry different data
» Age out after 1-hour…refreshed every 30minutes.

## Slide 4: Packet Types and Adjacencies
OSPF Packet Types
» Multiple OSPF Packet Types
• Hello
• Database Descriptor
• Link State Request
• Link State Update
• Link State Acknowledgment
» Most packets sent as multicasts

## Slide 5: OSPF Neighborship
» Hello packet contains some important information, which should match for a proper neighborship
• Hello and dead interval
• Authentication
• Area – ID
• Prefix-length
• Stub area flag

## Slide 6: Building Neighbor Relationships
» Exchange of Hello Packets
• May need to manually specify neighbor address depending on network type.
» Exchange of Database Descriptors
» Exchange of Link State Requests and Updates
» Fully Loaded

## Slide 7: OSPF DR & BDR Election
DR & BDR Election
» OSPF elects a DR (designated router) and a BDR (backup designated router) in broadcast and non-broadcast multi-access networks
» DR is responsible for sending an update to the neighbors that are received from other neighbors
» Special multicast address used for sending routing updates to DR/BDR: 224.0.0.6

## Slide 8: DR & BDR Election
» OSPF router with the highest priority becomes the DR
» OSPF router with lower priority than DR becomes BDR
» A BDR takes DR’s if DR fails
» Other OSPF routers are known as DROTHERS

## Slide 9: DR & BDR Election
» If OSPF priority has not been configured, highest router-id is referenced
» OSPF router with highest router-id becomes DR
» OSPF router with lower router-id than DR’s becomes the BDR

## Slide 10: Router-Identifier
» OSPF elects a router-id when the process comes up
» Router-id is elected on the basis of the given hierarchy.
• Router-id command under the OSPF instance
• Highest IP address of a loopback interface
• Highest IP address of a physically up/up interface

## Slide 11: Network Types, Router Roles, and Tables
OSPF Network Types (1)
» OSPF classifies links (network type) based on Layer-2 encapsulation.
» Network Type determines things such as:
• Can neighbors be discovered dynamically?
• How many neighbors are expected to be on the network?
• Is there a need for DR/BDR election?
» Type can be manually changed on some interfaces.

## Slide 12: OSPF Network Types (2)
» Broadcast
• Ethernet, Token Ring, FDDI
» Point-to-Point
• Loopback interfaces, PPP, HDLC
» Non Broadcast Multi-access
• Frame-Relay
» Point-to-Multipoint

## Slide 13: OSPF Router Roles
» Internal Router
» Backbone Router
» Area Border Router (ABR)
» Autonomous System Boundary Router (ASBR)

## Slide 14: OSPF Tables
» Neighbor table
• Contains neighbor information
» Link-State Database
• Contains database information
» SPF-Tree
» Routing table
• Contains best route on the basis of link cost

## Slide 15: Implementing OSPF
Configuration
» Initial OSPF Configuration commands
• Router(config)# router ospf <process-id>
• Router(config-router)# network <network-id> <WC mask> area < area-id>
• Router(config-router)# router-id <router-id>
» Configuring OSPF Interface priority
• Router(config-interface)# ip ospf priority <priority>
» Both the router-id and priority need OSPF instance reset to take effect after they are changed

## Slide 16: Verification
» Verification commands
• Router# show ip ospf neighbor
• Router# show ip ospf interface
• Router# show ip ospf database
• Router# show ip route ospf

## Slide 17: Troubleshooting OSPF
» Troubleshooting commands
• Router# debug ip ospf adjacency
• Router# debug ip packets
» Area-id, prefix mask, and authentication should match each other

## Slide 18: OSPF Cost
OSPF Metric
» Cost
» Like Spanning-Tree, OSPF Cost based on interface bandwidth
» The greater the BW…the lower the Cost
» Best path to any given network = path with lowest OSPF cost
» Can be configured explicitly, or affected by changing interface bandwidth.

## Slide 19: Configuration
» Configuring OSPF Interface Cost
• Router(config-interface)# ip ospf cost <value>
» Modifying interface Bandwidth
• Router(config-interface)# bandwidth <value>

## Slide 20: Verification
» Verification commands
• Router# show ip ospf interface
• Router# show ip route ospf

## Slide 21: Implementing OSPFv3
OSPFv3 Theory
» Similarities to IPv4 OSPF (OSPF v2)
• Same OSPF message types (Hello, LS-Update, etc)
• Uses same SPF algorithm, LSDB, and Metric
• Requires a Router-ID (32-bit)
• Same process for neighbor discovery and establishment
» Differences with OSPF v3
• Neighbors formed with Link Local addresses
• Neighbors don’t need same global prefixes on same link.
• Changes to name/functionality of some LSAs

## Slide 22: OSPFv3
» Enabling OSPFv3
• Router(config)# ipv6 unicast routing
• Router(config)# ipv6 router ospf <number>
• Router(config-router)# router-id <address>
• Router(config-router)# exit
» Applying OSPFv3
• Router(config-if)# ipv6 ospf <number> area <area-id>

## Slide 23: Verifying OSPFv3
» Verification commands
• Router# show ipv6 ospf neighbor
• Router# show ipv6 ospf database
• Router# show ipv6 route ospf
• Router# show ipv6 protocols