## Slide 1: Network Address Translation

## Slide 2: Introduction to NAT
» Separates LAN from WAN and provides accessibility to the outside world » Translates RFC1918 space addresses into public addresses » Provides security » Helps reduce public IP address consumption » Hides private addresses from outsiders

## Slide 3: Public and private addresses
» Private addresses cannot go outside the network » At least one public address is required for a private host to communicate to the Internet » Public IP addresses are globally routable

## Slide 4: Types of NAT
» Static NAT » Dynamic NAT » PAT (Port Address Translation)

## Slide 5: Static NAT
» One to one mapping » One private host requires a public IP address » Usually deployed at server end

## Slide 6: Configuring Static NAT
» Configuration commands • Router(config-if)# ip nat inside • Router(config-if)# ip nat outside • Router( config)# ip nat inside source static <private address> < public address>

## Slide 7: Verifying Static NAT
» Verification commands • Router# show ip nat translation

## Slide 8: Dynamic NAT
» Many to many mapping » One private host requires a public IP address obtained from a pool of available addresses. » Usually deployed for hosts utilizing DHCP. » Easier from the perspective of scalability

## Slide 9: Configuring Dynamic NAT
» Configuration commands • Router(config-if)# ip nat inside • Router(config-if)# ip nat outside • Router(config# access-list < acl no> <permit | deny > <source-address> <wildcard mask> • Router(config)# ip nat pool <name> <start-ip> <end-ip> netmask <subnet mask> • Router( config)# ip nat inside source list < acl no> pool <name>

## Slide 10: Verifying Dynamic NAT
» Verification commands • Router# show ip nat translation

## Slide 11: Port Address Translation (PAT)
» Port Address Translation » One to many mapping » One public address can provide multiple host connections » Usually deployed at client end » Easier from the perspective of scalability

## Slide 12: Configuring PAT
» Configuration commands • Router(config-if)# ip nat inside • Router(config-if)# ip nat outside • Router(config# access-list < acl no> <permit | deny > <source-address> <wildcard mask> • Router( config)# ip nat inside source list < acl no> interface <type/number> overload

## Slide 13: Verifying PAT
» Verification commands • Router# show ip nat translation