## Slide 1: Introduction to IPV4, TCP and UDP

## Slide 2: Introduction to IPv4
Internet Protocol version 4
Resides at OSI Layer-3 (Network Layer)
Connectionless(does not verify if the destination exists)
It is a routed protocol

## Slide 3: Common IP protocol values

## Slide 4: Introduction to IPV4
32-bit addressing system
Logical address for a network defined by IANA
IPv4 addresses are comprised of 4 octets
Dotted decimal notation is used to segment the octet

## Slide 5: Introduction to IPV4

## Slide 6: Communication Types
Unicast
• One-to-one communication
Multicast
• One-to-many communication
Broadcast
• One-to-all communication

## Slide 7: DHCP
Dynamic Host Configuration Protocol
• Dynamic assignment of IP information
• Based on older BootP protocol
• Client / Server
• Utilizes UDP (port 67 and 68)

## Slide 8: DNS
Domain Name Service
Used by computers to resolve names to IP addresses.
Typically uses UDP port 53.
DNS server responds to DNS requests
• Host sends DNS A-Record query
• DNS server responds with A-Record query response.

## Slide 9: OSI Transport Layer - UDP
Predominant protocols used at Layer-4
• TCP (Transmission Control Protocol)
• UDP (User Datagram Protocol)
UDP
• Connectionless

## Slide 10: OSI Transport Layer - TCP
Transmission Control Protocol
• Connection-oriented

## Slide 11: TCP 3 way handshake