## Slide 1: Wireless LANs

## Slide 2: Working With Wi-Fi
What is Wi-fi
It is the manipulation of electromagnetic radiation to encode the data
it is known as radio frequencies. There is huge spectrum of the electromagnetic waves

## Slide 3: Wi-fi standardization
Physical layer: how can increase the range of wi-fi. How can we encode more data using different methods
Mac layer: how can we secure the data

## Slide 4: 80.11 Phy standards
Frequency is just a general measurement term for measuring how often something changes over time. The unit of measurement of frequency is Hz. 1 Hz means something changing 1 time per sec.

## Slide 6: Wi-Fi Components
High power source longer we can send signals
More number of Antennas helps us to receive traffic smoothly. Antennas will convert the electrical signals into electromagnetic waves.
Transceiver is the combination of transmitter and receiver

## Slide 7: Access-Points

## Slide 8: Wi-fi Controller
Everything is managed by controller. The client access to the wi-fi i.e. authentication is also done by the clontroller

## Slide 9: Wi-Fi Network Types & Terminology

## Slide 10: Types of wi-fi network
Mesh: AP connected to each other on wireless. Like the situation in park if one AP doesn’t connect to the wired environment it will send data to the other AP on wireless.
AP connected to the wired network is known as the RAP(root AP) and Aps in mesh is known as MAP(mesh AP)

## Slide 11: General Wi-fi terms
BSS- the area up to which the AP signals can cover
Beacon --- it is sent by the AP to tell the client about its existance. Beacons are sent 10 times per sec. Inside the beacons the MAC address will be there of AP.
BSSID- the MAC address of the AP is called BSSID

## Slide 12: General Wi-Fi terms

## Slide 14: Wi-Fi Bands and Channels
ISM bands: ( industrial scientific and medical)
We know that wifi deals with radio frequencies and radio frequencies are he small subset of the large electromagnetic spectrum. By its nature EMR oscillates at certain frequencies.
All EMR which are oscillating is given certain name or label
Certain frequencies are allocated for certain purposes. So certain frequencies which are oscillating at certain rates you have to pay for them if you want to transmit on those frequencies . Some of the frequencies are there for free public use. These are called ISM band

## Slide 15: What is a Wi-fi channel
Channel is the collection of different frequencies working together

## Slide 16: Non overlapping channel
In an environment with multiple BSS, channels must be selected that don’t overlap

## Slide 17: Wi-fi channel design

## Slide 19: WLAN Architectures & Controllers
Autonomous WLAN Architectures

## Slide 20: Autonomous decision and challenges

## Slide 21: Autonomous Architecture

## Slide 23: Split MAC WLAN Architectures

## Slide 24: Split MAC WLAN Architectures
The real time function means the physical layer functions, it is going to deal with the radio frequencies, encryptions, collision etc.

## Slide 25: What is split?

## Slide 26: Split mac architecture

## Slide 27: CAPWAP

## Slide 28: CAPWAP tunnels

## Slide 29: CAPWAP tunnels

## Slide 30: CAPWAP tunnels for control

## Slide 31: CAPWAP tunnel for data

## Slide 32: CAPWAP tunnel packet format

## Slide 34: Cisco WLAN Controllers
Categories of WLAN controllers

## Slide 35: Embedded Wireless
WLAN functionality is embedded within another network device(typically a switch)

## Slide 36: Cisco Mobility Express
WLAN controller functionality is built into certain models of cisco access points

## Slide 37: Infrastructure Connections Of WLAN Components
Connections of WLAN components

## Slide 38: Wireless Infrastructure connections

## Slide 39: Access point physical interfaces

## Slide 40: Controller Physical Interfaces

## Slide 41: LAG